## Slide 1: Introduction to Operating Systems
CPSC/ECE 3220 Summer 2018
Lecture Notes
OSPP Chapter 7 – Part A
(adapted by Mark Smotherman from Tom Anderson’s slides on OSPP web site)

## Slide 2: Main Points
Scheduling policy: what to do next, when there are multiple threads ready to run
  Or multiple packets to send, or web requests to serve, or …
Definitions
  Response time, throughput, predictability
Uniprocessor policies
  FIFO, Round Robin (RR), optimal
  Multilevel feedback (MFQ) as approx. of optimal

## Slide 3: Example
You manage a web site that suddenly becomes wildly popular. Do you?
  Buy more hardware?
  Implement a different scheduling policy?
  Turn away some users? Which ones?
How much worse will performance get if the web site becomes even more popular?

## Slide 4: Definitions
Task/Job
  User request: e.g., mouse click, web request, shell command, …
Latency/response time
  How long does a task take to complete?
Throughput
  How many tasks can be done per unit of time?
Overhead
  How much extra work is done by the scheduler?
Fairness
  How equal is the performance received by different users?
Predictability
  How consistent is the performance over time?
Notes: 1. Minimize response time: elapsed time to do an operation (or job)
Response time is what the user sees: elapsed time to
echo a keystroke in editor
compile a program
run a large scientific problem
2. Maximize throughput: operations (or jobs) per second
Throughput is related to response time, but they're not identical -- for example, I’ll show that minimizing response time will lead you to do more context switching than you would if you were only concerned with throughput.
Two parts to maximizing throughput
a. Minimize overhead (for example, context switching)
b. Efficient use of system resources (not only CPU, but disk, memory, etc.)
What does CPU scheduling have to do with efficient use of the disk? A lot! Have to have CPU to make a disk request.
3. Fair: share CPU among users in some equitable way
Tradeoff: will argue you can get better average response time by making system less fair.
What does fairness mean?
Minimize # of angry phone calls? Minimize my response time?
Minimize average response time? We will argue fairness is a tradeoff against average response time; can get better average response time by making system less fair. Sort of like capitalism.
Anecdote: Response time has a lot to do with perceived effectiveness.
IBM keystroke experiment -- consistency is better than speed.
Might believe that since have PC's, CPU scheduling is less important -- usually, only one thing running at a time, for a single user. But! Face similar problems in networks -- how do you allocate scarce resources among users? Do you optimize for response time, throughput, fairness? In networks, fairness is often suboptimal.

## Slide 5: More Definitions
Workload
  Set of tasks for system to perform
Preemptive scheduler
  If we can take resources away from a running task
Work-conserving
  Resource is used whenever there is a task to run
  For non-preemptive schedulers, work-conserving is not always better
Scheduling algorithm
  Takes a workload as input
  Decides which tasks to do first
  Performance metric (throughput, latency) as output
  Only preemptive, work-conserving schedulers to be considered

## Slide 6: First In First Out (FIFO)
Schedule tasks in the order they arrive
  Continue running them until they complete or give up the processor
Example: memcached
  Facebook cache of friend lists, …
On what workloads is FIFO particularly bad?

## Slide 7: Shortest Job First (SJF) Premeptive
Always do the task that has the shortest remaining amount of work to do
  Often called Shortest Remaining Time First (SRTF) or Shortest Remaining Time Next (SRTN)
Suppose we have five tasks arrive one right after each other, but the first one is much longer than the others
  Which completes first in FIFO? Next?
  Which completes first in SJF(preemptive)? Next?
Notes: Need to be careful: optimal wrt average response time.
Recall: only preemptive schedulers.

## Slide 8: FIFO vs. SJF(preemptive)
Notes: Now you can see why SJF improves average response time – it runs short jobs first. Effect on the short jobs is huge; effect on the long job is small.

## Slide 9: Question
Claim: SJF(preemptive) is optimal for average response time
  Why?
Does SJF(preemptive) have any downsides?
Notes: Consider a hypothetical alternative policy that is not SJF, but that we think might be optimal. Because the alternative is not SJF, at some point it will choose to run a task that is longer than something else in the queue. If we now switch the order of tasks, keeping everything the same, but doing the shorter task first, we will reduce the average response time.
Downsides: starvation, and variance in response time. Some task might take forever!
Imagine a supermarket that used SJF – would it work?
What would you do if you went to the supermarket and they were using SJF? Clever person would go through with one item at a time…

## Slide 10: Question
Is FIFO ever optimal?
Pessimal?
Notes: Optimal = SJF
Pessimal = LJF

## Slide 11: Relationships Among 5 “Time” Values
Wait time
Arrival time
Response time
Service time
Completion time
Wait time (if any) precedes service time in FIFO
Wait time and service time can be intermixed in other policies

## Slide 12: Range of Classic Policies
Policies that do not use service times:
  FIFO – easiest to implement
  RR
  MFQ
Future knowledge policies – decisions made based on knowledge of service times:
  SJF(non-preemptive)
  SJF(preemptive) – minimum avg. response time
  Approximate SJF(preemptive) by predicting service times
    E.g., based on running average of CPU burst lengths, file sizes

## Slide 13: Round Robin
Each task gets resource for a fixed period of time = time quantum (or time slice)
  If task doesn’t complete, it goes back in line
Need to pick a time quantum
  What if time quantum is too long?
    Infinite?
  What if time quantum is too short?
    One instruction?
  Rule of thumb: 80%+ of tasks finish in one quantum
Notes: Can we combine best of both worlds? RR approximates SJF by moving long tasks to the end of the line.

## Slide 14: Round Robin
Notes: Approximation depends on granularity

## Slide 15: Round Robin vs. FIFO
Assuming zero-cost time slice, is Round Robin always better than FIFO?
Notes: Show of hands!
What’s the worst case for RR? Same sized jobs – then you are time-slicing for no purpose. Worse, this is nearly pessimal for average response time.

## Slide 16: Round Robin vs. FIFO
Notes: Everything is fair, but average response time in this case is awful – everyone finishes very late! In fact, this case is exactly when FIFO is optimal, RR is poor.
On the other hand, if we’re running streaming video, RR is great – everything happens in turn. SJF maximizes variance. But RR minimizes it.

## Slide 17: Round Robin = Fairness?
Is Round Robin always fair?
What is fair?
  FIFO?
  Equal share of the CPU?
  What if some tasks don’t need their full share?
  Minimize worst case divergence?
    Time task would take if no one else was running
    Time task takes under scheduling algorithm
Notes: Show of hands! After all, round robin ensures we don’t starve, and gives everyone a turn, but lets short tasks complete before long tasks.

## Slide 18: Policy vs. Mechanism
Policy = decision-making rule
  “what to do”
Mechanism = hardware or software that is used to implement a policy
  “how to do it”
What are mechanisms for Round Robin?

## Slide 19: Mixed Workload
Notes: One task does I/O repetively
The other tasks consume the CPU.
I/O task has to wait its turn for the CPU, and the result is that it gets a tiny fraction of the performance it could get.
By contrast the compute bound job gets almost as much as it would if the I/O task wasn’t there.
We could shorten the RR quantum, and that would help, but it would increase overhead.
what would this do under SJF? Every time the task returns to the CPU, it would get scheduled immediately!

## Slide 20: Max-Min Fairness
How do we balance a mixture of repeating tasks:
  Some I/O bound, need only a little CPU
  Some compute bound, can use as much CPU as they are assigned
One approach: maximize the minimum allocation given to a task
  If any task needs less than an equal share, schedule the smallest of these first
  Split the remaining time using max-min
  If all remaining tasks need at least equal share, split evenly
Notes: On previous slide, what would happen if we used max-min fairness? Then I/O task would be scheduled immediately – its always the one using less than its equal share.

## Slide 21: Multi-level Feedback Queue (MFQ)
Set of Round Robin queues
  Each queue has a separate priority
High priority queues have short time slices
  Low priority queues have long time slices
Scheduler picks first thread in highest priority queue
Tasks start in highest priority queue
  If time slice expires, task drops one level

## Slide 22: MFQ
Notes: What strategy should you adopt if you knew you were running on an MFQ system?

## Slide 23: Uniprocessor Summary (1)
FIFO is simple and minimizes overhead
If tasks are variable in size, then FIFO can have very poor average response time
If tasks are equal in size, FIFO is optimal in terms of average response time
Considering only the processor, SJF(preemptive) is optimal in terms of average response time
SJF(preemptive) is pessimal in terms of variance in response time

## Slide 24: Uniprocessor Summary (2)
If tasks are variable in size, Round Robin approximates SJF
If tasks are equal in size, Round Robin will have very poor average response time
Tasks that intermix processor and I/O benefit from SJF(preemptive) and can do poorly under Round Robin

## Slide 25: Uniprocessor Summary (3)
Max-Min fairness can improve response time for I/O-bound tasks
Round Robin and Max-Min fairness both avoid starvation

## Slide 26: Simulation Comparisons
fcfs results:
1-th 10-percentile avg. wait is 19.800 |******************
2-th 10-percentile avg. wait is 21.796 |********************
3-th 10-percentile avg. wait is 19.908 |******************
4-th 10-percentile avg. wait is 18.432 |*****************
5-th 10-percentile avg. wait is 19.444 |******************
6-th 10-percentile avg. wait is 19.618 |******************
7-th 10-percentile avg. wait is 19.984 |******************
8-th 10-percentile avg. wait is 21.264 |********************
9-th 10-percentile avg. wait is 21.188 |********************
10-th 10-percentile avg. wait is 18.490 |*****************
+--------------------
scaled to max value
overall avg. 19.992
rr results:
1-th 10-percentile avg. wait is 4.932 |**
2-th 10-percentile avg. wait is 5.164 |**
3-th 10-percentile avg. wait is 5.142 |**
4-th 10-percentile avg. wait is 9.858 |***
5-th 10-percentile avg. wait is 9.696 |***
6-th 10-percentile avg. wait is 15.340 |*****
7-th 10-percentile avg. wait is 19.858 |*******
8-th 10-percentile avg. wait is 26.128 |*********
9-th 10-percentile avg. wait is 35.976 |************
10-th 10-percentile avg. wait is 61.794 |********************
+--------------------
scaled to max value
overall avg. 19.389
mlfq results:
1-th 10-percentile avg. wait is 2.690 |*
2-th 10-percentile avg. wait is 2.808 |*
3-th 10-percentile avg. wait is 3.262 |*
4-th 10-percentile avg. wait is 7.084 |***
5-th 10-percentile avg. wait is 6.562 |**
6-th 10-percentile avg. wait is 6.566 |**
7-th 10-percentile avg. wait is 24.858 |*******
8-th 10-percentile avg. wait is 33.758 |**********
9-th 10-percentile avg. wait is 34.030 |**********
10-th 10-percentile avg. wait is 68.922 |********************
+--------------------
scaled to max value
overall avg. 19.054
srtn results:
1-th 10-percentile avg. wait is 0.058 |
2-th 10-percentile avg. wait is 0.170 |
3-th 10-percentile avg. wait is 0.470 |
4-th 10-percentile avg. wait is 0.874 |
5-th 10-percentile avg. wait is 1.234 |*
6-th 10-percentile avg. wait is 2.286 |*
7-th 10-percentile avg. wait is 4.222 |**
8-th 10-percentile avg. wait is 7.232 |***
9-th 10-percentile avg. wait is 14.148 |******
10-th 10-percentile avg. wait is 47.980 |********************
+--------------------
scaled to max value
overall avg. 7.867